## Slide 1: Digital Video Processing
Introduction

## Slide 2: Digital Video
Digital video is a representation of a natural or real-world visual scene, sampled spatially or temporally

## Slide 3: Spatial Sampling
Sampling the signal at a point in time produces a sampled image or frame that has defined values at a set of sampling points.
The number of sampling points influences the visual quality of the image.
  Less sampling points  low-resolution image
  More sampling points  high-resolution image

## Slide 4: Spatial Sampling

## Slide 5: Temporal Sampling
Sampling images at a regular interval of time
  High sampling rate  smoother motion
  Low sampling rate  jerky motion

## Slide 6: Frames and Fields
A video signal may be sampled as a series of complete frames, progressive sampling, or as a sequence of interlaced fields, interlaced sampling.
In an interlaced video sequence, half of the data in a frame, one field, is typically sampled at each temporal sampling interval.
A field may consist of either the odd-numbered or even-numbered lines within a complete video frame and an interlaced video sequence typically contains a series of fields, each representing half of the information in a complete video frame

## Slide 7: Frames and Fields
Video sources with letter ‘i’ are called interlaced, video sources listed with letter ‘p’ are called progressive
  480i, 480p, 1080i, 1080p

## Slide 8: Digital Video
A scene is sampled at a point in time to produce a frame (a representation of the complete visual scene at that point in time) or a field (consisting of odd or even numbered lines of spatial samples). Sampling is repeated at intervals (e.g., 1/25 or 1/30 second intervals) to produce a moving video.

## Slide 9: Colour Space
A universally accepted method or standard chosen to represent brightness, luminance or luma and color is described as color space.

## Slide 10: YCrCb Color Space
The Y:Cr:Cb colour space is a popular way of efficiently representing colour images.
Y is the luminance component and can be calculated as a weighted average of R, G and B:
  Y = krR + kgG + kbB
  Where, k are weighting factors.

## Slide 11: YCrCb Color Space
The colour information can be represented as colour difference (chrominance or chroma) components, where each chrominance component is the difference between R, G or B and the luminance Y:
  Cr = R – Y
  Cg = G – Y
  Cb = B – Y

## Slide 12: YCrCb Color Space
An RGB image may be converted to Y:Cr:Cb after capture in order to reduce storage and/or transmission requirements.
The equations for converting an RGB image to and from Y:Cr:Cb colour space and vice versa are
Y = 0.299 R + 0.587 G + 0.114 B
Cb = 0.564(B – Y)
Cr = 0.713 (R – Y)
R = Y + 1.402Cr
G = Y – 0.344 Cb – 0.714Cr
B = Y + 1.772Cb